Midi16
<img showcase>
The Midi16 is a midi fighter inspired controller that I built after I got jump scared by the original controller’s price.
Material used in the project: 16 face arcade buttons, a side toggle button (from an old car radio), a front facing 2way temporary switch, a 3.5mm mono jack to use as a pedal input, a 128x64px monocolored OLED display (SSD1306), acrylic panels, some standoffs and screws, a USB type B to micro USB converter cable, an arduino pro micro, and a 16 channel multiplexer.

Links between boards/pieces:
16ch mtpx S0 - pin 15
16ch mtpx S1 - pin 14
16ch mtpx S2 - pin 16
16ch mtpx S3 - pin 10
16ch mtpx Sig - pin 9
Screen SCK - pin 3
Screen SDA - pin 2
Switch left - pin 4
Switch right - pin 5
Toggle button - pin 8
Jack - pin 18

The face buttons connect to the multiplexer in the following manner:
0 1 2 3
4 5 6 7
8 9 10 11
12 13 14 15

but while coding I translated the pattern to fit my needs by inverting the rows and now the buttons are interpreted as:
12 13 14 15
8 9 10 11
4 5 6 7
0 1 2 3

The side toggle button exchanges back and forward between “play mode” and “menu mode”.

While in menu mode the front switch changes menus (“debug” menu, transcribe menu and midi channel menu) and the face buttons select the options.